REAR TYRE RE-LOCA TOR FOR DISCOVERY SERIES I

Box Contents:

1 ea. Instruction Sheet

1 ea. Aluminum Mount Plate, anodized

3 ea. 16mm x 50mm Hex Head Bolts

9 ea. 16mm Nuts

3 ea. 16mm Lock Washers

You will need:

Discovery Series I Owner's Manual

Hacksaw, Sawzall or abrasive wheel (if you use install Option #2- Recommended Install)

Touch-up Paint (if you use install Option #2- Recommended Install)

24mm Socket and Wrench

INSTRUCTIONS:

This instruction sheet covers two types of install options. Option #1 is the Bolt-on Install and Option #2, the recommended Install, which requires you to cut the factory studs. (We recommend this install, as it keeps the weight of the tire closer to the carrier. )

INSTALL OPTION #1- BOLT-ON INSTALL

- Remove your spare tire as per the instructions located in your owner's manual.

- Install two 16mm nuts on each factory stud. These nuts become a spacer between the factory carrier and the Aluminum Mount Plate. Snug-up the first nut, and then do the same with the second. NOTE -these do not have to excessively tightened.

- Slide the Aluminum Mount Plate over the factory studs. Installone 16mm lock washer and nut onto each stud. Tighten these bolts securely as they will hold your tire to the vehicle.

- Install your spare tire onto the new mounting studs. Install your factory spare lug-nuts and tighten as needed to secure the wheel.

INSTALL OPTION #2- RECOMMENDED

- Remove your spare tire per the instructions in your owner's manual.

- Install one nut to the bottom of each factory stud and then mark each one approximately 15/16" from the carrier. (Masking tape works great to mark.)

- Using a Hacksaw, Sawzall or abrasive wheel cut the factory studs on the mark made in prior step.  (CAUTION must be used when using any type of powered equipment. Please follow all of the instructions and warnings included with your tools. We strongly recommend safety glasses).  Remove the nut you installed in Step #2 to clean the threads. Smooth all studs with a file or similar tool.  To prevent rust, re-paint the cut studs.

- Slide the Aluminum Mount Plate over the factory studs. Install a 16mm lock washer and one nut onto each stud. Tighten these bolts securely as they will hold your tire to the vehicle.

- Install your spare tire onto the new mounting studs. Install your factory spare lug-nuts and tighten as needed to secure the wheel.